## Slide 1
Lecture 01: Digital System Design
Dept. of Computer Sc. and Engg.
University of Rajshahi
www.ru.ac.bd
Dr. Mahboob Qaosar &
Dr. Shamim Ahmad

## Slide 2: Number Systems
Decimal (Base 10)
  10 digits (0,1,2,3,4,5,6,7,8,9)
Binary (Base 2)
  2 digits (0,1)
    Digits are often called bits (binary digits)
Hexadecimal (Base 16)
  16 digits (0-9,A,B,C,D,E,F)
    Often referred to as Hex

## Slide 3: Number Systems

## Slide 4: Positional Notation
Each digit is weighted by the base(r) to the positional power
N = dn-1dn-2 …d0.d1d2…dm
  = (dn-1x r n-1 ) + (dn-2x r n-1 ) + … + (d0 1x r0 ) +
  (d1x r1) + (d2 x r2) + … (dm x r m )
Example : 872.6410
(8 x 102) + (7 x 101) + (2 x 100)
+ (6 x 10-1) + (4 x 10-2)
Example: 1011.12 = ?
Example :12A16 = ?

## Slide 5: Positional Notation (Solutions to Example Problems)
872.6410 = 8x102 + 7x101 + 2x100 + 6x10-1 + 4 x10-2
        800 + 70 + 2 + .6 + .04

## Slide 6: Positional Notation (Solutions to Example Problems)
1011.12
= 1x23 + 0x22 + 1x21 + 1x20 + 1x2-1
      = 8 + 0 + 2 + 1 + .5
      = 11.510

## Slide 7: Positional Notation (Solutions to Example Problems)
12A16 = 1x162 + 2x161 + Ax160
      = 256 + 32 + 10
      = 29810

## Slide 8: Powers of Bases
2-3= .125
2-2= .25
2-1= .5 160 = 1
20 = 1 161 = 16 = 24
21 = 2 162 = 256 = 28
22 = 4 163 = 4096 = 212
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256 210 = 1024 = 1Kb
29 = 512 220 = 1,048,576 = 1Mb
210 = 1024 230 = 1,073,741,824 = 1Gb
211 = 2048
212 = 4096

## Slide 9: Determining What Base is being Used
Subscripts
  87410 10112 AB916
  AB9(16)
Prefix Symbols
  (None) 874 %1011 $AB9
Postfix Symbols
  AB9H

## Slide 10: Conversion from Base R to Decimal
Use Positional Notation
%11011011 = ?10
$3A94 = ?10

## Slide 11: Conversion from Binary to Decimal
Use Positional Notation
%11011011 = ?10 %11011011
= 1x27 + 1x26 + 1x24 + 1x23 + 1x21 + 1x20 = 128 + 64 + 16 + 8 + 2 + 1 = 21910

## Slide 12: Conversion from Hexadecimal to Decimal
3A9416 = ?10
3A9416 = 3x163 + Ax162 + 9x161 + 4x160
=12288 + 2560 + 144 + 4
=15996

## Slide 13: Conversion from Decimal to Base R
Use Successive Division
  Repeatedly divide by the desired base until 0 is reached
  Save the remainders as the final answer
  The first remainder is the LSB (least significant bit); the last remainder is the MSB (Most significant bit)
43710 = ?2
= 1101101012
43710 = ?16
= 1B516

## Slide 14: Conversion from Decimal to Binary
Use Successive Division
  Repeatedly divide by the desired base until 0 is reached
  Save the remainders as the final answer
  The first remainder is the LSB (least significant bit); the last remainder is the MSB (Most significant bit)
43710 = ?2
437 / 2 = 218 remainder 1
218 / 2 = 109 remainder 0
109 / 2 = 54 remainder 1
54 / 2 = 27 remainder 0
27 / 2 = 13 remainder 1
13 / 2 = 6 remainder 1
6 / 2 = 3 remainder 0
3 / 2 = 1 remainder 1
1 / 2 = 0 remainder 1
= 1101101012

## Slide 15: Conversion from Decimal to Hexadecimal
43710 = ?16
  437 / 16 = 27 remainder 5
  27 / 16 = 1 remainder 11 (11=B)
  1 / 16 = 0 remainder 1
42710 = 1B516

## Slide 16: Conversion from Binary to Hex
Starting at the LSB working left, group the bits by 4s. Padding of 0s can occur on the most significant group.
Convert each group of 4 into the equivalent HEX value.
%1101110101100 = $?
= $1BAC

## Slide 17: Conversion from Hex to Binary
Convert each HEX digit to the equivalent 4-bit binary grouping.
$A73 = %?
  = %101001110011

## Slide 18: Conversion of Fractions
Conversion from decimal to binary requires multiplying by the desired base (2)
0.62510 = ?2
= 0.101 2

## Slide 21: Addition/Subtraction of Binary Numbers
101011
+ 1
101100
101011
+ 001011
110110
The carry out has a weight equal to the base (in this case 16). The digit that left is the excess (Base – sum).

## Slide 22: Addition/Subtraction of Hex Numbers
$3A
+$28
$62
The carry out has a weight equal to the base (in this case 16). The digit that left is the excess (Base – sum).

## Slide 23: Signed Number Representation
Three ways to represent signed numbers
  Sign-Magnitude
  1s Complement
  2s Complement

## Slide 24: Sign-Magnitude
For an N-bit word, the most significant bit is the sign bit; the remaining bits represent the magnitude
0110 = +6
1110 = -6
Addition/subtraction of numbers can result in overflow (errors) – (Due to fixed number of bits); two values for zero
Range for n bits: -(2n-1–1) through (2n-1–1)

## Slide 25: 1’s Complement
Negative numbers = N’ = (2n-1–1) –P (where P is the magnitude of the number)
  For a 5-bit system, -7 = 11111 -00111
  11000
Range for n bits:-(2n-1–1) through (2n-1–1)

## Slide 26: 2’s Complement
Negative Numbers = N* = 2n – P
(where P is the magnitude of the number)
  For a 5-bit system, -7 = 100000
  -00111
  11001
Another way to form 2’s complement representation is to complement P and add 1
Range for n bits: -(2n-1) through (2n-1–1)

## Slide 27: Numbers Represented with 4-bit Fixed Digit Representation

## Slide 28: Summary of Signed Number Representations
Sign Magnitude – has two values for 0
- errors in addition of negative and positive numbers
1s complement – two values for 0
- additional hardware needed to compensate for this
2s Complement – representation of choice

## Slide 29: Unsigned/Signed Overflow
You can detect unsigned overflow if there is a carryout of the MSB.
You can detect signed overflow if the sum of two positive numbers is a negative number or if the sum of two negative numbers is a positive number. An overflow never occurs in an addition of a negative and a positive number.

## Slide 30: Codes
Decimal Codes
  BCD (Binary Coded Decimal)
    Weighted Codes (8421, 2421, etc…)
ASCII Codes
  ASCII (American Standard Code for Information Interchange)
  Unicode Standard
Unit Distance Codes
  Gray
Error Detection Codes
  Parity Bit
Error Correction Codes
  Hamming Code

## Slide 31: BCD Codes (Decimal Codes)
Coded Representations for the 10 decimal digits
Requires 4 bits (23 < 10 <24)
Only use 10 combinations of 16 possible combinations

## Slide 32: BCD Codes (Decimal Codes)
Weighted Code
  8421 code
    Most common
    Default
    The corresponding decimal digit is determined by adding the weights associated with the 1s in the code group.
    The BCD representation is NOT the binary equivalent of the decimal number
      62310 = 0110 0010 0011
  2421, 5421, etc… codes
    The weights associated with the bits in each code group are given by the name of the code

## Slide 33: BCD Codes (Decimal Codes)
Nonweighted Codes
  2-out-of-5
    Actually weighted 74210 except for the digit 0
    Used by the post office for scanning bar codes for zip codes
    Has error detection properties

## Slide 34: BCD Codes (Decimal Codes)
U.S. Postal Service bar code corresponding to the ZIP code 14263-1045.

## Slide 35: Unit Distance Codes
Important when converting analog to digital
Only one bit changes between successive integers
Gray Code is most popular example

## Slide 36: Unit Distance Codes
Angular position encoders.
Conventional binary encoder. (b) Gray code encoder.

## Slide 37: Unit Distance Codes
Angular position encoders with misaligned photosensing devices.
(a) Conventional binary encoder. (b) Gray code encoder.

## Slide 38: Mirror Image Conversion

## Slide 39: From Binary to a Gray-code
Copy MSB
Add this bit to the next position
  Record Sum
  Ignore Carry (if any)
Record successive sum until completed

## Slide 40: From Binary to Gray code
1 0 1 1
1 1 1 0

## Slide 41: From a Gray-code to Binary
Copy MSB
Add the Binary MSB to next Significant bit of Gray code
  Record Sum
  Ignore Carry (if any)
Continue process until LSB is reached

## Slide 42: From a Gray-code to Binary
1 0 1 1
1 1 0 1

## Slide 43: Digital Circuit

## Slide 44: Excess-3 code
Decimal
Binary
Decimal
Binary
Decimal
Binary
Decimal
Binary
−3
0000
1
0100
5
1000
9
1100
−2
0001
2
0101
6
1001
10
1101
−1
0010
3
0110
7
1010
11
1110
0
0011
4
0111
8
1011
12
1111
Within the range when 1’s complemented, apart from BCD

## Slide 46: ASCII Codes

## Slide 48: Unicode (Arabic)

## Slide 49: Unicode (Bengali)

## Slide 52: Hamming Code
Number the bits starting from 1: bit 1, 2, 3, 4, 5, etc.
Write the bit numbers in binary. 1, 10, 11, 100, 101, etc.
All bit positions that are powers of two (have only one 1 bit in the binary form of their position) are parity bits.
All other bit positions, with two or more 1 bits in the binary form of their position, are data bits.
Each data bit is included in a unique set of 2 or more parity bits, as determined by the binary form of its bit position.
In general each parity bit covers all bits where the binary AND of the parity position and the bit position is non-zero.

## Slide 53: Hamming Code
Parity bit 1 covers all bit positions which have the least significant bit set: bit 1 (the parity bit itself), 3, 5, 7, 9, etc.
Parity bit 2 covers all bit positions which have the second least significant bit set: bit 2 (the parity bit itself), 3, 6, 7, 10, 11, etc.
Parity bit 4 covers all bit positions which have the third least significant bit set: bits 4–7, 12–15, 20–23, etc.
Parity bit 8 covers all bit positions which have the fourth least significant bit set: bits 8–15, 24–31, 40–47, etc.

## Slide 54
Example

## Slide 55: Example
p2
d1
p3
d2
d3
d4
p4
d5
d6
d7
Data word (without parity):
0
1
1
0
1
0
1
p1
0
1
0
1
1
p2
0
0
1
0
0
1
p3
0
1
1
0
p4
0
1
0
1
Data word (with parity):
p1
1
1
0
0
0
1
1
0
0
1
0
1
Calculation of Hamming code parity bits

## Slide 56: Example
The new data word (with parity bits) is now "10001100101".
We now assume the final bit gets corrupted and turned from 1 to 0.
Our new data word is "10001100100";
How the Hamming codes were created we flag each parity bit as 1 when the even parity check fails.

## Slide 57: Example
p1
p2
d1
p3
d2
d3
d4
p4
d5
d6
d7
Parity check
Parity bit
Received data word:
1
0
0
0
1
1
0
0
1
0
0
p1
1
0
1
0
1
0
Fail
1
p2
0
0
1
0
0
0
Fail
1
p3
0
1
1
0
Pass
0
p4
0
1
0
0
Fail
1
Checking of parity bits (switched bit highlighted)

## Slide 58: Example
The final step is to evaluate the value of the parity bits
It goes furthest to the right
The integer value of the parity bits is 11, signifying that the 11th bit in the data word (including parity bits) is wrong and needs to be flipped.

## Slide 59: Example
p4
p3
p2
p1
Binary
1
0
1
1
Decimal
8
2
1
Σ = 11
Flipping the 11th bit changes 10001100100 back into 10001100101.
Removing the Hamming codes gives the original data word of 0110101.

## Slide 61: How Much Memory?
Memory is purchased in bits –
  How many bits do I need if I want to distinguish between 8 colors?
  How many bits do I need if I want to represent 16 million different colors?

## Slide 62: How Much Memory?
How many bits do I need if I want to distinguish between 8 colors?
2x-1 < 8 <= 2x
x = 3 (3 bits are needed)
How many bits do I need if I want to represent 16 million different colors?
2x-1 < 16 million <= 2x
16M = 1Mx16 = 220x24 = 224
x = 24 (24 bits are needed)