## Slide 1
Lecture 02: Digital System Design
Dept. of Computer Sc. and Engg.
University of Rajshahi
www.ru.ac.bd
Dr. Mahboob Qaosar

## Slide 2: Binary Logic
Deals with binary variables that take 2 discrete values (0 and 1), and with logic operations
Three basic logic operations:
  AND, OR, NOT
Binary/logic variables are typically represented as letters: A,B,C,…,X,Y,Z

## Slide 3: Binary Logic Function
F(vars) = expression
Example: F(a,b) = a’•b + b’
G(x,y,z) = x•(y+z’)
set of binary
variables
Operators ( +, •, ‘ )
Variables
Constants ( 0, 1 )
Groupings (parenthesis)

## Slide 4: Basic Logic Operators
AND
OR
NOT
F(a,b) = a•b, F is 1 if and only if a=b=1
G(a,b) = a+b, G is 1 if either a=1 or b=1
H(a) = a’, H is 1 if a=0
Binary
Unary

## Slide 5: Basic Logic Operators (cont.)
1-bit logic AND resembles binary multiplication:
0 • 0 = 0, 0 • 1 = 0,
1 • 0 = 0, 1 • 1 = 1
1-bit logic OR resembles binary addition, except for one operation:
0 + 0 = 0, 0 + 1 = 1,
1 + 0 = 1, 1 + 1 = 1 (≠ 102)

## Slide 6: Truth Tables for logic operators
Truth table: tabular form that uniguely represents the relationship between the input variables of a function and its output
A | B | F=A•B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
2-Input AND
A | B | F=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
2-Input OR
A | F=A’
0 | 1
1 | 0
NOT

## Slide 7: Truth Tables (cont.)
Q: Let a function F() depend on n variables. How many rows are there in the truth table of F() ?
A: 2n rows, since there are 2n possible binary patterns/combinations for the n variables

## Slide 8: Logic Gates
Logic gates are abstractions of electronic circuit components that operate on one or more input signals to produce an output signal.
2-Input AND
2-Input OR
NOT (Inverter)
A
A
A
B
B
F
G
H
F = A•B
G = A+B
H = A’

## Slide 9: Timing Diagram
A
B
F=A•B
G=A+B
H=A’
1
1
1
1
1
0
0
0
0
0
t0
t1
t2
t3
t4
t5
t6
Input
signals
Gate
Output
Signals
Basic
Assumption:
Zero time for
signals to
propagate
Through gates
Transitions

## Slide 10: Combinational Logic Circuit from Logic Function
Consider function F = A’ + B•C’ + A’•B’
A combinational logic circuit can be constructed to implement F, by appropriately connecting input signals and logic gates:
  Circuit input signals  from function variables (A, B, C)
  Circuit output signal  function output (F)
  Logic gates  from logic operations
A
B
C
F

## Slide 11: Combinational Logic Circuit from Logic Function (cont.)
In order to design a cost-effective and efficient circuit, we must minimize the circuit’s size (area) and propagation delay (time required for an input signal change to be observed at the output line)
Observe the truth table of F=A’ + B•C’ + A’•B’ and G=A’ + B•C’
Truth tables for F and G are identical  same function
Use G to implement the logic circuit (less components)
A | B | C | F | G
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 12: Combinational Logic Circuit from Logic Function (cont.)
A
B
C
F
A
B
C
G

## Slide 13: Boolean Algebra
VERY nice machinery used to manipulate (simplify) Boolean functions
George Boole (1815-1864): “An investigation of the laws of thought”
Terminology:
  Literal: A variable or its complement
  Product term: literals connected by •
  Sum term: literals connected by +

## Slide 14: Boolean Algebra Properties
Let X: boolean variable, 0,1: constants
X + 0 = X -- Zero Axiom
X • 1 = X -- Unit Axiom
X + 1 = 1 -- Unit Property
X • 0 = 0 -- Zero Property

## Slide 15: Boolean Algebra Properties (cont.)
Let X: boolean variable, 0,1: constants
X + X = X -- Idepotence
X • X = X -- Idepotence
X + X’ = 1 -- Complement
X • X’ = 0 -- Complement
(X’)’ = X -- Involution

## Slide 16: Duality
The dual of an expression is obtained by exchanging (• and +), and (1 and 0) in it, provided that the precedence of operations is not changed.
Cannot exchange x with x’
Example:
  Find H(x,y,z), the dual of F(x,y,z) = x’yz’ + x’y’z
  H = (x’+y+z’) (x’+y’+ z)

## Slide 17: Duality (cont’d)
With respect to duality, Identities 1 – 8 have the following relationship:
1. X + 0 = X 2. X • 1 = X (dual of 1)
3. X + 1 = 1 4. X • 0 = 0 (dual of 3)
5. X + X = X 6. X • X = X (dual of 5)
7. X + X’ = 1 8. X • X’ = 0 (dual of 8)

## Slide 18: More Boolean Algebra Properties
Let X,Y, and Z: boolean variables
10. X + Y = Y + X -- Commutative
11. X • Y = Y • X -- do
12. X + (Y+Z) = (X+Y) + Z -- Associative
13. X•(Y•Z) = (X•Y)•Z -- Associative
14. X•(Y+Z) = X•Y + X•Z -- Distributive
15. X+(Y•Z) = (X+Y) • (X+Z) -- Distributive
16. (X + Y)’ = X’ • Y’
17. (X • Y)’ = X’ + Y’ -- DeMorgan’s
In general,
( X1 + X2 + … + Xn )’ = X1’•X2’ • … •Xn’, and
( X1•X2•… •Xn )’ = X1’ + X2’ + … + Xn’

## Slide 19: Absorption Property
x + x•y = x
x•(x+y) = x (dual)
Proof: x + x•y = x•1 + x•y = x•(1+y) = x•1 = x

## Slide 20: Power of Duality
x + x•y = x is true, so (x + x•y)’=x’
(x + x•y)’=x’•(x’+y’)
x’•(x’+y’) =x’
Let X=x’, Y=y’
X•(X+Y) =X, which is the dual of x + x•y = x.
The above process can be applied to any formula. So if a formula is valid, then its dual must also be valid.
Proving one formula also proves its dual.

## Slide 21: Consensus Theorem
xy + x’z + yz = xy + x’z
(x+y)•(x’+z)•(y+z) = (x+y)•(x’+z) -- (dual)
Proof: xy + x’z + yz = xy + x’z + (x+x’)yz = xy + x’z + xyz + x’yz = (xy + xyz) + (x’z + x’zy) = xy + x’z

## Slide 22: Truth Tables (revisited)
Enumerates all possible combinations of variable values and the corresponding function value
Truth tables for some arbitrary functions F1(x,y,z), F2(x,y,z), and F3(x,y,z) are shown to the right.
x | y | z |  | F1 | F2 | F3
0 | 0 | 0 |  | 0 | 1 | 1
0 | 0 | 1 |  | 0 | 0 | 1
0 | 1 | 0 |  | 0 | 0 | 1
0 | 1 | 1 |  | 0 | 1 | 1
1 | 0 | 0 |  | 0 | 1 | 0
1 | 0 | 1 |  | 0 | 1 | 0
1 | 1 | 0 |  | 0 | 0 | 0
1 | 1 | 1 |  | 1 | 0 | 1

## Slide 23: Truth Tables (cont.)
Truth table: a unique representation of a Boolean function
If two functions have identical truth tables, the functions are equivalent (and vice-versa).
Truth tables can be used to prove equality theorems.
However, the size of a truth table grows exponentially with the number of variables involved, hence unwieldy. This motivates the use of Boolean Algebra.

## Slide 24: Boolean expressions-NOT unique
Unlike truth tables, expressions representing a Boolean function are NOT unique.
Example:
  F(x,y,z) = x’•y’•z’ + x’•y•z’ + x•y•z’
  G(x,y,z) = x’•y’•z’ + y•z’
The corresponding truth tables for F() and G() are to the right. They are identical.
Thus, F() = G()
x | y | z |  | F | G
0 | 0 | 0 |  | 1 | 1
0 | 0 | 1 |  | 0 | 0
0 | 1 | 0 |  | 1 | 1
0 | 1 | 1 |  | 0 | 0
1 | 0 | 0 |  | 0 | 0
1 | 0 | 1 |  | 0 | 0
1 | 1 | 0 |  | 1 | 1
1 | 1 | 1 |  | 0 | 0

## Slide 25: DeMorgan’s Theorem #1
(A · B)’ = A’ + B’
EQUAL

## Slide 26: DeMorgan’s Theorem #2
(A + B)’ = A’ · B’
EQUAL

## Slide 27: Algebraic Manipulation
Boolean algebra is a useful tool for simplifying digital circuits.
Why do it? Simpler can mean cheaper, smaller, faster.
Example: Simplify F = x’yz + x’yz’ + xz. F = x’yz + x’yz’ + xz = x’y(z+z’) + xz = x’y•1 + xz = x’y + xz

## Slide 28: Algebraic Manipulation (cont.)
Example: Prove x’y’z’ + x’yz’ + xyz’ = x’z’ + yz’
Proof: x’y’z’+ x’yz’+ xyz’ = x’y’z’ + x’yz’ + x’yz’ + xyz’ = x’z’(y’+y) + yz’(x’+x) = x’z’•1 + yz’•1 = x’z’ + yz’ QED.

## Slide 29: Complement of a Function
The complement of a function is derived by interchanging (• and +), and (1 and 0), and complementing each variable.
Otherwise, interchange 1s to 0s in the truth table column showing F.
The complement of a function IS NOT THE SAME as the dual of a function.

## Slide 30: Complementation: Example
Find G(x,y,z), the complement of F(x,y,z) = xy’z’ + x’yz
G = F’ = (xy’z’ + x’yz)’ = (xy’z’)’ • (x’yz)’ DeMorgan = (x’+y+z) • (x+y’+z’) DeMorgan again
Note: The complement of a function can also be derived by finding the function’s dual, and then complementing all of the literals

## Slide 31: More Logic Gates
We can construct any combinational circuit with AND, OR, and NOT gates
Additional logic gates are used for practical reasons

## Slide 32: NAND and NOR Gate

## Slide 33: NAND Gate
Known as a “universal” gate because ANY digital circuit can be implemented with NAND gates alone.
To prove the above, it suffices to show that AND, OR, and NOT can be implemented using NAND gates only.

## Slide 34: NAND Gate as an Inverter Gate
X | Z
0 | 1
1 | 0
X
(Before Bubble)
Equivalent to Inverter
Notes: When you tie the inputs on a NAND gate together, the output will be the complement of the input.

## Slide 35: NAND Gate as an AND Gate
X | Y | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X
Y
NAND Gate
Inverter
Equivalent to AND Gate
Notes: This one is easy to see, a NAND gate is an AND gate with the output inverted. So if you invert the output again, you will get an AND gate. Note that we are using a NAND gate for the inverter.

## Slide 36: NAND Gate as an OR Gate
X | Y | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Equivalent to OR Gate
X
Y
NAND Gate
Inverters
Notes: This one is a bit harder to see. If you invert both of the inputs of a NAND gate, you will get an OR gate. Note that we’re using NAND gates as inverters.

## Slide 37: NOR Gate
Also a “universal” gate because ANY digital circuit can be implemented with NOR gates alone.
This can be similarly proven as with the NAND gate.

## Slide 38: NOR Gate as an Inverter Gate
X | Z
0 | 1
1 | 0
X
(Before Bubble)
Equivalent to Inverter
Notes: When you tie the inputs on a NOR gate together, the output will be the complement of the input.

## Slide 39: NOR Gate as an OR Gate
X | Y | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
X
Y
NOR Gate
“Inverter”
Equivalent to OR Gate
Notes: This one is easy to see, a NOR gate is in NOR gate with the output inverted. So if you invert the output again you will get an OR gate. Note we’re using a NOR gate for the inverter.

## Slide 40: NOR Gate as an AND Gate
X | Y | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Equivalent to AND Gate
X
Y
NOR Gate
“Inverters”
Notes: This one is a bit harder to see. If you invert both the inputs of a NOR gate you will get an AND gate. Note we’re using NOR gates as inverters.

## Slide 41: XOR and XNOR
X | Y | F = XY
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Y
F
XOR: “not-equal” gate
X | Y | F = XY
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X
Y
F
XNOR: “equal” gate
X

## Slide 42: Exclusive-OR (XOR) Function
XOR (also ) : the “not-equal” function
XOR(X,Y) = X  Y = X’Y + XY’
Identities:
  X  0 = X
  X  1 = X’
  X  X = 0
  X  X’ = 1
Properties:
  X  Y = Y  X
  (X  Y)  W = X  ( Y  W)

## Slide 43: XOR circuit with 4 NANDs

## Slide 44: Karnaugh Maps
Karnaugh maps (K-maps) are graphical representations of boolean functions.
One map cell corresponds to a row in the truth table.
Also, one map cell corresponds to a minterm or a maxterm in the boolean expression
Multiple-cell areas of the map correspond to standard terms.

## Slide 45: Two-Variable Map
m3
m2
1
m1
m0
0
1
0
x1
x2
0
1
2
3
NOTE: ordering of variables is IMPORTANT for f(x1,x2), x1 is the row, x2 is the column.
Cell 0 represents x1’x2’; Cell 1 represents x1’x2; etc. If a minterm is present in the function, then a 1 is placed in the corresponding cell.
m3
m1
1
m2
m0
0
1
0
x2
x1
0
2
1
3
OR

## Slide 46: Two-Variable Map (cont.)
Any two adjacent cells in the map differ by ONLY one variable, which appears complemented in one cell and uncomplemented in the other.
Example: m0 (=x1’x2’) is adjacent to m1 (=x1’x2) and m2 (=x1x2’) but NOT m3 (=x1x2)

## Slide 47: 2-Variable Map -- Example
f(x1,x2) = x1’x2’+ x1’x2 + x1x2’ = m0 + m1 + m2 = x1’ + x2’
1s placed in K-map for specified minterms m0, m1, m2
Grouping (ORing) of 1s allows simplification
What (simpler) function is represented by each dashed rectangle?
  x1’ = m0 + m1
  x2’ = m0 + m2
Note m0 covered twice
x1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
x2
0
1
2
3

## Slide 48: Minimization as SOP using K-map
Enter 1s in the K-map for each product term in the function
Group adjacent K-map cells containing 1s to obtain a product with fewer variables. Group size must be in power of 2 (2, 4, 8, …)
Handle “boundary wrap” for K-maps of 3 or more variables.
Realize that answer may not be unique

## Slide 49: Three-Variable Map
m6
m7
m5
m4
1
m2
m3
m1
m0
0
10
11
01
00
yz
x
0
1
3
2
4
5
7
6
-Note: variable ordering is (x,y,z); yz specifies column, x specifies row.
-Each cell is adjacent to three other cells (left or right or top or bottom or edge wrap)

## Slide 50: Three-Variable Map (cont.)
The types of structures that are either minterms or are generated by repeated application of the minimization theorem on a three variable map are shown at right. Groups of 1, 2, 4, 8 are possible.
minterm
group of 2 terms
group of 4 terms

## Slide 51: Simplification
Enter minterms of the Boolean function into the map, then group terms
Example: f(a,b,c) = a’c + abc + bc’
Result: f(a,b,c) = a’c+ b
 | 1 | 1 | 1
 |  | 1 | 1
a
bc
 | 1 | 1 | 1
 |  | 1 | 1

## Slide 52: More Examples
f1(x, y, z) = ∑ m(2,3,5,7)
f2(x, y, z) = ∑ m (0,1,2,3,6)
f1(x, y, z) = x’y + xz
f2(x, y, z) = x’+yz’
yz X | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 |  | 1 | 1 | 
1 | 1 | 1 | 1
 |  |  | 1

## Slide 53: Four-Variable Maps
Top cells are adjacent to bottom cells. Left-edge cells are adjacent to right-edge cells.
Note variable ordering (WXYZ).
m10
m11
m9
m8
10
m14
m15
m13
m12
11
m6
m7
m5
m4
01
m2
m3
m1
m0
00
10
11
01
00
WX
YZ

## Slide 54: Four-variable Map Simplification
One square represents a minterm of 4 literals.
A rectangle of 2 adjacent squares represents a product term of 3 literals.
A rectangle of 4 squares represents a product term of 2 literals.
A rectangle of 8 squares represents a product term of 1 literal.
A rectangle of 16 squares produces a function that is equal to logic 1.

## Slide 55: Example
Simplify the following Boolean function (A,B,C,D) = ∑m(0,1,2,4,5,7,8,9,10,12,13).
First put the function g( ) into the map, and then group as many 1s as possible.
cd
ab
1
1
1
1
1
1
1
1
1
1
1
g(A,B,C,D) = c’+b’d’+a’bd
1
1
1
1
1
1
1
1
1
1
1

## Slide 56: Don't Care Conditions
There may be a combination of input values which
  will never occur
  if they do occur, the output is of no concern.
The function value for such combinations is called a don't care.
They are denoted with x or –. Each x may be arbitrarily assigned the value 0 or 1 in an implementation.
Don’t cares can be used to further simplify a function

## Slide 57: Minimization using Don’t Cares
Treat don't cares as if they are 1s to generate PIs.
Delete PI's that cover only don't care minterms.
Treat the covering of remaining don't care minterms as optional in the selection process (i.e. they may be, but need not be, covered).

## Slide 58: Example
Simplify the function f(a,b,c,d) whose K-map is shown at the right.
f = a’c’d+ab’+cd’+a’bc’
or
f = a’c’d+ab’+cd’+a’bd’
x
x
1
1
x
x
0
0
1
0
1
1
1
0
1
0
x
x
1
1
x
x
0
0
1
0
1
1
1
0
1
0
0 | 1 | 0 | 1
1 | 1 | 0 | 1
0 | 0 | x | x
1 | 1 | x | x
ab
cd
00
01
11
10
00
01
11
10

## Slide 59: Another Example
Simplify the function g(a,b,c,d) whose K-map is shown at right.
g = a’c’+ ab or
g = a’c’+b’d
x | 1 | 0 | 0
1 | x | 0 | x
1 | x | x | 1
0 | x | x | 0
x | 1 | 0 | 0
1 | x | 0 | x
1 | x | x | 1
0 | x | x | 0
x | 1 | 0 | 0
1 | x | 0 | x
1 | x | x | 1
0 | x | x | 0
ab
cd