## Slide 1
Lecture 03: Digital System Design
Dept. of Computer Sc. and Engg.
University of Rajshahi
www.ru.ac.bd
Dr. Mahboob Qaosar

## Slide 2: 1-bit Adder
Performs the addition of two binary bits.
Four possible operations:
  0+0=0
  0+1=1
  1+0=1
  1+1=10
Circuit implementation requires 2 outputs; one to indicate the sum and another to indicate the carry.

## Slide 3: Half Adder
Performs 1-bit addition.
Inputs: A, B
Outputs: S, C
Index indicates significance, 0 is for LSB and 1 is for the next higher significant bit.
Boolean equations:
  S = AB’+A’B = A  B
  C = AB
1
0
1
1
0
1
0
1
0
1
1
0
0
0
0
0
C
S
B
A
Truth Table

## Slide 4: Half Adder (cont.)
S = AB’+A’B = A B
C = AB
1 bit
half adder
A
B
C
S
Block Diagram

## Slide 5: n-bit Addition
Design an n-bit binary adder which performs the addition of two n-bit binary numbers and generates a n-bit sum and a carry out.
Example: Let n=4 Cout C3 C2 C1 C0 1 1 0 1 0
A3 A2 A1 A0 1 1 0 1 + B3 B2 B1 B0 + 1 1 0 1 --------------------- --------------- S3 S2 S1 S0 1 1 0 1 0

## Slide 6: Full Adder
Full adder (for higher-order bit addition)
Combinational circuit that performs the additions of 3 bits (two bits and a carry-in bit)
1 bit
full adder
Ai
Bi
Ci+1
Si
Ci

## Slide 7: Full Adder (cont.)
1
0
1
1
0
0
1
0
0
1
1
0
1
0
1
1
0
0
1
1
1
1
1
1
1
0
1
0
Ci
0
1
1
0
0
1
0
0
0
0
0
0
Ci+1
Si
Bi
Ai
The K-maps for
  Ci+1:
  Si:
1
1
1
0
0
1
0
0
BiCi
Ai
0
1
0
1
1
0
1
0
BiCi
Ai

## Slide 8: Full Adder (cont.)
Boolean equations:
  Ci+1 = AiBi + AiCi + BiCi
  Si = AiBi’ Ci’ + Ai’Bi’Ci + Ai’BiCi’ + AiBiCi = Ai  Bi  Ci
You can design full adder circuit directly from the above equations (requires 3 ANDs and 1 OR for Ci+1 and 2 XORs for Si)

## Slide 9: Full Adder using 2 Half Adders
A full adder can also be realized with two half adders and an OR gate, since Ci+1 can also be expressed as:
Ci+1 = AiBiCi + AiBiCi’ + AiBi’Ci + Ai’BiCi
= AiBi(Ci + Ci’) + (AiBi’ + Ai’Bi)Ci = AiBi + (Ai  Bi)Ci
and Si = Ai  Bi  Ci
Ai
Bi
Ci
Ci+1
Si

## Slide 10: n-bit Combinational Adders
Perform parallel multi-bit addition
Ripple Carry Adder
  Simple design
  Time consuming.
Carry Look ahead Adder
  More complex than ripple-carry adder
  Reduces circuit delay

## Slide 11: n-bit Ripple Carry Adder
Constructed using n 1-bit full adder blocks in parallel.
Cascade the full adders so that the carry out from one becomes the carry in to the next higher bit position.

## Slide 12: Example: 4-bit Ripple Carry Adder
C4 C3 C2 C1 C0 A3 A2 A1 A0 +B3 B2 B1 B0 -------------- S3 S2 S1 S0

## Slide 13
Implement subtraction with 2’s complement number system
A-B = A + (-B) = A + 1’sc (B) + 1
Implement 1’sc with XOR gates:
Binary Subtractor

## Slide 14
4-Bit Binary Adder/Subtractor
Binary Adder/Subtractor

## Slide 15: Ripple Carry Adder Delay
Circuit delay in an n-bit ripple carry adder is determined by the delay on the carry path from the LSB (C0) to the MSB (Cn).
Let the delay in a 1-bit FA be Δ. Then, the delay of an n-bit ripple carry adder is nΔ.

## Slide 16: Carry Look ahead Adder
Alternative design for a combinational n-bit adder.
Practical design with reduced delay at the expense of more complex hardware.
Derived from a transformation of the ripple carry adder design.

## Slide 17: Carry Lookahead Adder Design
From a FA, separate between carry generation (a new carry signal is generated, i.e. Cout=1) and carry propagation (an existing Cin is propagated to Cout)
Generate: Gi = AiBi: if 1, Ci+1=1
Propagate: Pi = Ai  Bi: if 1, Ci+1 = Ci
Partial Full Adder (PFA)
Full Adder (FA)
Bi
Bi
Ai
Ci
Ci
Ci+1
Si
Si
Gi
Pi
Ai

## Slide 18: Carry Lookahead Adder Design (cont.)
Ci+1 = Gi + PiCi
PFA design breaks S functionality apart from G/P functionality

## Slide 19: Carry Look ahead Adder (cont.)
Does this (design in previous slide) solve the long delay problem?
No, carry out still “ripples” !
Idea: use two levels of logic to generate carry out of any block Ci in terms of carry in C0 and addend bits Ai and Bi

## Slide 20: Block CLA
Implement:
  C1 = G0+P0 C0
  C2 = G1+P1C1 = G1+P1(G0+P0C0) = G1+P1G0+P1P0C0
  C3 = G2 + P2C2 = G2+P2G1+P2P1G0+P2P1P0C0
  C4 = G3+P3G2+P3P2G1+P3P2P1G0 + P3P2P1P0 C0 = G0-3 + P0-3C0
Group carry generate
Group carry propagate

## Slide 21: Generate/Propagate logic of a 4-bit CLA
-- C0 … Cn-1 have a 2-gates delay
-- C4 = G0-3+P0-3C0
has a 3-gates delay

## Slide 22: BCD Adder

## Slide 23: BCD adder
BCD adder can’t exceed 9 on each input digit. K is the carry.

## Slide 24: Rules of BCD adder
When the binary sum is greater than 1001, we obtain a non-valid BCD representation.
The addition of binary 6(0110) to the binary sum converts it to the correct BCD representation and also produces an output carry as required.
To distinguish them from binary 1000 and 1001, which also have a 1 in position Z8, we specify further that either Z4 or Z2 must have a 1.
C = K + Z8Z4 + Z8Z2

## Slide 25: Implementation of BCD adder
A decimal parallel adder that adds n decimal digits needs n BCD adder stages.
The output carry from one stage must be connected to the input carry of the next higher-order stage.
If =1
0110

## Slide 26: Comparator

## Slide 27
Inputs |  | Outputs |  | 
B | A | A > B | A = B | A < B
0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 Bit Digital Comparator Truth Table