## Slide 1
Lecture 04: Digital System Design
Dept. of Computer Sc. and Engg.
University of Rajshahi
www.ru.ac.bd
Dr. Mahboob Qaosar

## Slide 2: Decoders
A combinational circuit that converts binary information from n coded inputs to a maximum 2n coded outputs  n-to- 2n decoder
n-to-m decoder, m ≤ 2n
Examples: BCD-to-7-segment decoder, where n=4 and m=10

## Slide 3
Decoders (cont.)

## Slide 4
2-to-4 Decoder

## Slide 5: 3-to-8 Decoder
Three inputs, A0, A1, A2, are decoded into eight outputs, D0 through D7
Each output Di represents one of the minterms of the 3 input variables.
Di = 1 when the binary number A2A1A0 = i
Shorthand: Di = mi
The output variables are mutually exclusive; exactly one output has the value 1 at any time, and the other seven are 0.

## Slide 6: The truth table of 3-to-8 Decoder
A2 | A1 | A0 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 |  |  |  |  |  |  | 
0 | 0 | 1 |  | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  | 1 |  |  |  |  | 
0 | 1 | 1 |  |  |  | 1 |  |  |  | 
1 | 0 | 0 |  |  |  |  | 1 |  |  | 
1 | 0 | 1 |  |  |  |  |  | 1 |  | 
1 | 1 | 0 |  |  |  |  |  |  | 1 | 
1 | 1 | 1 |  |  |  |  |  |  |  | 1

## Slide 7: 3-to-8 Decoder

## Slide 8: 3-to-8 Decoder with Enable

## Slide 9
3-to-8-line decoder using nand-gates

## Slide 10: Implementation of the Boolean expressions f1(x2,x1,x0) = m(1,2,4,5) and f2(x2,x1,x0) = m(1,5,7) with a 3-to-8-line decoder and two or-gates.

## Slide 11: Implementation of the Boolean expressions f1(x2,x1,x0) = m(0,1,3,4,5,6) = !m(2,7) and f2(x2,x1,x0) = m(1,2,3,4,6) = !m(0,5,7) with a 3-to-8-line decoder and two nor-gates.

## Slide 12: f1(x2,x1,x0) = M(0,1,3,5) f2(x2,x1,x0) = M(1,3,6,7) (a) Using output or-gates. (b) Using output nor-gates.

## Slide 13: Realization of the pair of maxterm canonical expressions f1(x2,x1,x0) = M(0,3,5) and f2(x2,x1,x0) = M(2,3,4) with a 3-to-8-line decoder and two and-gates

## Slide 14: Realization of the Boolean expressions f1(x2,x1,x0) = M(0,1,3,4,7) = !M(2,5,6) and f2(x2,x1,x0) = M(1,2,3,4,5,6) = !M(0,7) with a 3-to-8-line decoder and two nand-gates.

## Slide 15: A decoder realization of f1(x2,x1,x0) = m(0,2,6,7) and f2(x2,x1,x0) = m(3,5,6,7) (a) Using output and-gates. (b) Using output nand-gates.

## Slide 16: Implementation of the Boolean expressions
E.g. use 74XX138,3-to-8 decoder to implement boolean functions
Y1=A’B’+AC+A’C’
Y2=A’C+AC’
Y3=B’C+BC’

## Slide 17: Implementation of the Boolean expressions
Y1=A’B’+AC+A’C’=m0+m1+m2+m5+m7
= (m0’m1’m2’m5’m7’)’
Y2=A’C+AC’= m1+m3+m4+m6
= (m1’m3’m4’m6’)’
Y3=B’C+BC’=m1+m2+m5+m6
= (m1’m2’m5’m6’)’

## Slide 18: Implementation of the Boolean expressions
Y1= (m0’m1’m2’m5’m7’)’
Y2= (m1’m3’m4’m6’)’
Y3= (m1’m2’m5’m6’)’

## Slide 19: Implementation of the Boolean expressions
Y1=A’B’+AC+A’C’=m0+m1+m2+m5+m7
=∑(0,1,2,5,7)
=∏(3,4,6)=M3M4M6=m3’m4’m6’
Y2=A’C+AC’= m1+m3+m4+m6
=m0’m2’m5’m7’
Y3=B’C+BC’=m1+m2+m5+m6
=m0’m3’m4’m7’

## Slide 20: Implementation of the Boolean expressions
Y1=m3’m4’m6’
Y2=m0’m2’m5’m7’
Y3=m0’m3’m4’m7’

## Slide 21: Implementation of the Boolean expressions
e.g. X=f(a,b,c)=∑(0,3,5,6,7)
=a’b’c’+ab+bc+ac

## Slide 22: Implementation of Binary Adder Using a Decoder
Another example: Recall full adder equations, and let X, Y, and Z be the inputs:
  S(X,Y,Z) = m(1, 2, 4, 7)
  C(X,Y,Z) = m(3, 5, 6, 7)
Since there are 3 inputs and a total of 8 minterms, we need a 3-to-8 decoder.

## Slide 23
S(X,Y,Z) = Σm(1,2,4,7)
C(X,Y,Z) = Σm(3,5,6,7)
Implementation of Binary Adder Using a Decoder

## Slide 24: Decoder Expansions
Larger decoders can be constructed using a number of smaller ones.
HIERARCHICAL design!
Example: A 6-to-64 decoder can be designed using four 4-to-16 and one 2-to-4 decoders. How? (Hint: Use the 2-to-4 decoder to generate the enable signals to the four 4-to-16 decoders).

## Slide 25: Decoder Expansions
Two 74XX138 decoders forming a single 4-to-16 decoder(P131)

## Slide 26: Decoder Expansions
A 5-to-32 decoder using one 2-to-4 and four 3-to-8 decoder ICs(P132)

## Slide 27: Encoders
An encoder is a digital circuit that performs the inverse operation of a decoder. An encoder has 2n input lines and n output lines.
The output lines generate the binary equivalent of the input line whose value is 1.

## Slide 28: Encoders (cont.)

## Slide 29: Encoder Truth Table
8-to-3 binary encoder (octal-to-binary)
A0 = D1 + D3 + D5 + D7
A1 = D2 + D3 + D6 + D7
A2 = D4 + D5 + D6 + D7

## Slide 30: An 8-to-3-line encoder
y0
y1
y2

## Slide 31
Encoder with active Flag
A = 1 if E = 1 and one xi = 1, otherwise A = 0

## Slide 32: Priority Encoder
  Accepts multiple values and encodes them
    Works when more than one input is active
  Consists of:
    Inputs (2n)
    Outputs
      when more than one output is active, sets output to correspond to highest input
      V (indicates whether any of the inputs are active)
    Selectors / Enable (active high or active low)
Notes: 32

## Slide 33
Example: 4-to-2 Priority Encoder Truth Table

## Slide 34
D3 | D2 | D1 | D0 | A1 | A2 | V
0 | 0 | 0 | 0 | x | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
4-to-2 Priority Encoder Truth Table

## Slide 35
4-to-2 Priority Encoder

## Slide 36: 8-to-3 Priority Encoder