## Slide 1
Lecture 05: Digital System Design
Dept. of Computer Sc. and Engg.
University of Rajshahi
www.ru.ac.bd
Dr. Mahboob Qaosar

## Slide 2: Multiplexer (MUX)
A MUX is a digital switch that has multiple inputs (sources) and a single output (destination).
The select lines determine which input is connected to the output.
MUX Types
   2-to-1 (1 select line)
   4-to-1 (2 select lines)
   8-to-1 (3 select lines)
   16-to-1 (4 select lines)
Multiplexer
Block Diagram
Select
Lines
Inputs
(sources)
Output
(destination)
1
2N
N
MUX

## Slide 3: Typical Application of a MUX
MP3 Player
Docking Station
Laptop
Sound Card
Digital
Satellite
Digital
Cable TV
Surround Sound System
MUX
D0
D1
D2
D3
Y
B | A | Selected Source
0 | 0 | MP3
0 | 1 | Laptop
1 | 0 | Satellite
1 | 1 | Cable TV
Multiple Sources
Single Destination
Selector
Notes: This slide shows a typical application of a multiplexer (in this case a 4-to-1 MUX). Have the students share other common applications of MUXs.
http://images.tigerdirect.ca/skuimages/large/Logitech-X-540-L23-7250-mai.jpg

## Slide 4: Example: A 4-to-1 Multiplexer
I0
A 4-to-1 Multiplexer:
I1
I2
I3
S0
S1
F
1 output
n control inputs
2n inputs
Enable (G)

## Slide 5
S1 | S0 | F
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
4-to-1 Multiplexer
Notes: 5

## Slide 6: 4-to-1 Multiplexer Waveforms
I0 |  |  |  |  |  |  |  | 
I1 |  |  |  |  |  |  |  | 
I2 |  |  |  |  |  |  |  | 
I3 |  |  |  |  |  |  |  | 
S0 |  |  |  |  |  |  |  | 
S1 |  |  |  |  |  |  |  | 
F |  |  |  |  |  |  |  | 
 | I0 | I1 | I2 | I3 | I0 | I1 | I2 | I3
Input
Data
Select
Line
Output
Data
Notes: Waveform diagram for a 4-to-1 MUX. The input data signals (D0-D3) are colored RED to indicate when its is connected to the output Y. Note: There is no significance to the values of the four input data signals; they are intended solely to demonstrate that the select lines (A & B) will select what input data signal will be connected to the output.

## Slide 7
Cascading multiplexers
Using three 2-1 MUX to make one 4-1 MUX
S1 | S0 | F
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
F
Notes: 7

## Slide 8
F
2-1
MUX
S E
S2 E
S2 | S1 | S0 | F
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7
I0
I1
I2
I3
I4
I5
I6
I7
Example: Construct an
8-to-1 multiplexer using
2-to-1 multiplexers.
Notes: 8

## Slide 9
A Multiplexer uses n binary select bits to choose from a maximum of 2n unique input lines.
Multiplexers and decoders both can decode minterms.
Decoders have n number of output lines while multiplexers have only one output line.
The decoded minterms are used to select data from one of up to 2n unique data input lines.
The output of the multiplexer is the data input whose index is specified by the n bit code.
Multiplexer Versus Decoder
Notes: 9

## Slide 10: Multiplexer Versus Decoder
Note that the multiplexer has an extra OR gate. A1 and A0 are the two inputs in decoder. There are four inputs plus two selecs in multiplexer.
4-to-1 Multiplexer
2-t0-4 Decoder
Notes: 10

## Slide 11: Demultiplexer (DEMUX)
A DEMUX is a digital switch with a single input (source) and a multiple outputs (destinations).
The select lines determine which output the input is connected to.
DEMUX Types
   1-to-2 (1 select line)
   1-to-4 (2 select lines)
   1-to-8 (3 select lines)
   1-to-16 (4 select lines)
Demultiplexer
Block Diagram
Select
Lines
Input
(source)
Outputs
(destinations)
2N
1
N
DEMUX
Notes: This slide explains the function of a demultiplexer.

## Slide 12: Typical Application of a DEMUX
Single Source
Multiple Destinations
Selector
D0
D1
D2
D3
X
DEMUX
B | A | Selected Destination
0 | 0 | B/W Laser Printer
0 | 1 | Fax Machine
1 | 0 | Color Inkjet Printer
1 | 1 | Pen Plotter
B/W Laser
Printer
Color Inkjet
Printer
Pen
Plotter
Fax
Machine
Notes: This slide shows a typical application of a demultiplexer (in this case a 1-to-4 DEMUX). Ask students to share other common applications of DEMUXs.

## Slide 13: 1-to-4 De-Multiplexer (DEMUX)
S1 | S0 | D0 | D1 | D2 | D3
0 | 0 | X | 0 | 0 | 0
0 | 1 | 0 | X | 0 | 0
1 | 0 | 0 | 0 | X | 0
1 | 1 | 0 | 0 | 0 | X
D0
D1
D2
D3
X
S1 S0
DEMUX
S1 S0
Notes: SSI logic diagram, block diagram, and truth table for a 1-to-4 De-MUX

## Slide 14: 1-to-4 De-Multiplexer Waveforms
X |  |  |  |  |  |  |  | 
S0 |  |  |  |  |  |  |  | 
S1 |  |  |  |  |  |  |  | 
D0 |  |  |  |  |  |  |  | 
D1 |  |  |  |  |  |  |  | 
D2 |  |  |  |  |  |  |  | 
D3 |  |  |  |  |  |  |  | 
Output
Data
Select
Line
Input
Data
Notes: Waveform diagrams for a 1-to-4 De-MUX. The output signals (D0-D3) are colored RED to indicate when its is connected to the input X. Note: There is no significance to the value of the input data signal; it is intended solely to demonstrate that the select lines (A & B) will determine what output signal is connected to the input.

## Slide 15
End